## Slide 1: CPUs
CPU performance.
CPU power consumption and power management.
Safety and security.

## Slide 2: Elements of CPU performance
Cycle time.
CPU pipeline.
Memory system.

## Slide 3: Pipelining
Several instructions are executed simultaneously at different stages of completion.
Various conditions can cause pipeline bubbles that reduce utilization:
  branches;
  memory system delays;
  etc.

## Slide 4: Performance measures
Latency: time it takes for an instruction to get through the pipeline.
Throughput: number of instructions executed per time period.
Pipelining increases throughput without reducing latency.

## Slide 5: ARM7 pipeline
ARM 7 has 3-stage pipe:
  fetch instruction from memory;
  decode opcode and operands;
  execute.

## Slide 6: ARM pipeline execution
add r0,r1,#5
sub r2,r3,r6
cmp r2,#3
fetch
time
decode
fetch
execute
decode
fetch
execute
decode
execute
1
2
3

## Slide 7: Pipeline stalls
If every step cannot be completed in the same amount of time, pipeline stalls.
Bubbles introduced by stall increase latency, reduce throughput.

## Slide 8: ARM multi-cycle LDMIA instruction
fetch
decode
ex ld r2
ldmia
r0,{r2,r3}
sub
r2,r3,r6
cmp
r2,#3
ex ld r3
fetch
time
decode
ex sub
fetch
decode
ex cmp

## Slide 9: Control stalls
Branches often introduce stalls (branch penalty).
  Stall time may depend on whether branch is taken.
May have to squash instructions that already started executing.
Don’t know what to fetch until condition is evaluated.

## Slide 10: ARM pipelined branch
time
fetch
decode
ex bne
bne foo
sub
r2,r3,r6
fetch
decode
foo add
r0,r1,r2
ex bne
fetch
decode
ex add
ex bne

## Slide 11: Delayed branch
To increase pipeline efficiency, delayed branch mechanism requires n instructions after branch always executed whether branch is executed or not.
SHARC supports delayed and non-delayed branches.
  Specified by bit in branch instruction.
  2 instruction branch delay slot.

## Slide 12: Example: ARM execution time
Determine execution time of FIR filter:
  for (i=0, f=0; i<N; i++)
  f = f + c[i]*x[i];
Only branch in loop test may take more than one cycle.
  BLT loop takes 1 cycle best case, 3 worst case.

## Slide 13: FIR filter ARM code
; loop initiation code
MOV r0,#0 ; use r0 for i, set to 0
MOV r8,#0 ; use a separate index for arrays
ADR r2,N ; get address for N
LDR r1,[r2] ; get value of N
MOV r2,#0 ; use r2 for f, set to 0
ADR r3,c ; load r3 with address of base of c
ADR r5,x ; load r5 with address of base of x
; test for exit
loop CMP r0,r1
BGE loopend ; if I >= N, exit loop
; loop body
LDR r4,[r3,r8] ; get value of c[i]
LDR r6,[r5,r8] ; get value of x[i]
MUL r4,r4,r6 ; compute c[i]*x[i]
ADD r2,r2,r4 ; add into running sum
; update
ADD r8,r8,#4 ; add one to array index
ADD r0,r0,#1 ; add 1 to i
B loop
loopend ...

## Slide 14: FIR filter block diagram
initiation
test
body
update
tinit
ttest
tbody
tupdate
executed once
executed N times
executed N+1 times

## Slide 15: FIR filter performance by block
Block | Variable | # instructions | # cycles
Initiation | tinit | 7 | 7
Test | ttest | 2 | [2,4]
Body | tbody | 4 | 4
Update | tupdate | 3 | 4
tloop = tinit+ N(tbody + tupdate + ttest,best) + ttest,worst
Loop exit succeeds is worst case
Loop exit fails is best case

## Slide 16: PIC16F execution time
Instruction divided into four Q cycles:
  Q1 decodes.
  Q2 reads operands.
  Q3 performs data operations.
  Q4 writes data.
One Q cycle per clock cycle.
Execution time for one instruction is Tcy.

## Slide 17: PIC16F instruction timing
Most instructions execute in one cycle, except:
  CALL, GOTO, RETFIE, RETLW, RETURN require 2 cycles.
  Skip-if instructions require two cycles if skip is taken.

## Slide 18: PIC16F loop execution timing
This program sets a bit on an I/O device for a data-dependent amount of time.
Computed goto determines number of bsfs executed.
  len=1 -> go to len3, etc.
movf len, w ; get ready for computed goto
addwf pcl, f ; computed goto (PCL is low byte of PC)
len3: bsf x, I ; set the bit at t-3
len2: bsf x,l ; set the bit at t-2
len1: bsf x,l ; set the bit at t-1
bcf x, l ; clear the bit at t

## Slide 19: C55x pipeline
C55x has 7-stage pipe:
  fetch;
  decode;
  address: computes data/branch addresses;
  access 1: reads data;
  access 2: finishes data read;
  Read stage: puts operands on internal busses;
  execute.

## Slide 20: C55x organization
Instruction
unit
Program
flow
unit
Address
unit
Data
unit
3 data read busses
3 data read address busses
program address bus
program
read bus
2 data write busses
2 data write address busses
16
24
24
16
24
32
Instruction
fetch
Data read
from memory
D bus
Single operand
read
C, D busses
Dual operand
read
B bus
Dual-multiply
coefficient
Writes

## Slide 21: C55x pipeline hazards
Processor structure:
  Three computation units.
  14 operators.
Can perform two operations per instruction.
Some combinations of operators are not legal.

## Slide 22: C55x hazards
A-unit ALU/A-unit ALU.
A-unit swap/A-unit swap.
D-unit ALU,shifter,MAC/D-unit ALU,shifter,MAC
D-unit shifter/D-unit shift, store
D-unit shift, store/D-unit shift, store
D-unit swap/D-unit swap
P-unit control/P-unit control

## Slide 23: Memory system performance
Caches introduce indeterminacy in execution time.
  Depends on order of execution.
Cache miss penalty: added time due to a cache miss.

## Slide 24: Types of cache misses
Compulsory miss: location has not been referenced before.
Conflict miss: two locations are fighting for the same block.
Capacity miss: working set is too large.

## Slide 25: CPU power consumption
Most modern CPUs are designed with power consumption in mind to some degree.
Power vs. energy:
  heat depends on power consumption;
  battery life depends on energy consumption.

## Slide 26: CMOS power consumption
Voltage drops: power consumption proportional to V2.
Toggling: more activity means more power.
Leakage: basic circuit characteristics; can be eliminated by disconnecting power.

## Slide 27: CPU power-saving strategies
Reduce power supply voltage.
Run at lower clock frequency.
Disable function units with control signals when not in use.
Disconnect parts from power supply when not in use.

## Slide 28: C55x low power features
Parallel execution units---longer idle shutdown times.
Multiple data widths:
  16-bit ALU vs. 40-bit ALU.
Instruction caches minimizes main memory accesses.
Power management:
  Function unit idle detection.
  Memory idle detection.
  User-configurable IDLE domains allow programmer control of what hardware is shut down.

## Slide 29: Power management styles
Static power management: does not depend on CPU activity.
  Example: user-activated power-down mode.
Dynamic power management: based on CPU activity.
  Example: disabling off function units.

## Slide 30: Power-down costs
Going into a power-down mode costs:
  time;
  energy.
Must determine if going into mode is worthwhile.
Can model CPU power states with power state machine.

## Slide 31: ARMv8-A standby mode
Standby keeps power on CPU but stops or gates most clocks.
WFI instruction waits for interrupt or debug request.
WFE instruction waits for certain specified events.

## Slide 32: Application: NXP LPC 1311
Four power modes:
  Run: normal operation.
  Sleep: stops CPU clock, with CPU and peripheral logic still powered. Peripherals may initiate interrupts that wake up the CPU.
  Deep sleep: stops CPU clock, powers down most analog blocks, maintains CPU and peripheral registers and SRAM values.
  Deep power-down: power and clocks shut down to entire chip, registers and SRAM not maintained.

## Slide 33: LPC1311 power state machine
run
sleep
deep sleep
Prun = 56 mW
Psleep = 6.6 mW
Pdeep sleep = 89 mA
2.9 ms
23.6 ms
deep power-down
Pdeep power-down = 667 nA
240 ms

## Slide 34: Power management
Different physical mechanisms require different strategies:
  Dynamic voltage and frequency scaling (DVFS) for low leakage.
  Race-to-dark for high leakage.
Total energy consumption comes from dynamic and static power consumption mechanisms:

## Slide 35: Two power management strategies
DVFS used for cases when power consumption is dominated by dynamic power.
Characteristics as a function of power supply voltage:
  Clock frequency proportional to power supply.
  Power consumption proportional to square of power supply.
Reducing power supply voltage reduces performance but reduces power consumption more.
Adjust power supply voltage to level just fast enough for current tasks.
Race-to-dark used when power consumption is dominated by static power.
Run as fast as possible, then remove power supply from logic to eliminate static power consumption.

## Slide 36: Safety and security
Programs that perform important operations should run in trusted mode.
Supervisor mode, memory management provide some level of trust but does not ensure that the code comes from a trusted source.
Testing a digital signature for software before executing ensures that the software comes from a trusted source.

## Slide 37: Trusted programs and root of trust
Checking a digital signature for code requires a public key.
  Public key must come from a trusted source.
A trusted program may rely on another trusted program, etc.
  New program’s level of trustworthiness depends on the previous program’s trustworthiness.
Trust must eventually be traced back to a root of trust that provides known trust.
Root of trust can be provided with a hardware key that cannot be altered.

## Slide 38: Chain-of-trust
root-of-trust
trusted environment 1
trusted environment 2
untrusted environment 1

## Slide 39: ARM Trusted Execution Environment
Four-compartment model:
  Normal world includes user and system modes.
  Hypervisor mode supports virtual machines.
  Trusted World partitions into secure and non-secure components.
  SecurCore provides physically separate chips for additional protection.
Trusted Execution Environment (TEE) provides secure execution mode.

## Slide 40: Secure operation according to ARM
Processor security mechanisms should limit system access.
DMA should provide secure access for memory and I/O.
Access to CPU from other parts of system should be limited.
Trusted software should be able to identify and control processes that consume resources in the non-trusted world.
JTAG etc. should not compromise security.
I/O devices should support secure/non-secure operation.
Platform should have a unique, non-modifiable key.
Platform should provide secure trusted private key storage.
Process and update should be secure and verifiable.
Secure execution should ensure that control flow cannot be subverted.
Platform should provide security primitives.

## Slide 41: Smart cards
Smart cards are used for financial, medical, other types of secure information.
  Must operate at very low energy levels and very low cost.
Runs from extneral power supply.
Some code held in ROM.
Permanent storage in non-volatile EEPROM.
Cryptography engine provides low power operation, trusted functions.
CPU
ROM
RAM
EEPROM
crypto
I/O