## Slide 1: Program design and analysis
Software modem.

## Slide 2: Theory of operation
Frequency-shift keying:
  separate frequencies for 0 and 1.
time
0
1

## Slide 3: FSK encoding
Generate waveforms based on current bit:
bit-controlled
waveform
generator
0110101

## Slide 4: FSK decoding
A/D converter
zero filter
one filter
detector
0 bit
detector
1 bit

## Slide 5: Transmission scheme
Send data in 8-bit bytes. Arbitrary spacing between bytes.
Byte starts with 0 start bit.
Receiver measures length of start bit to synchronize itself to remaining 8 bits.
start (0)
bit 1
bit 2
bit 3
bit 8
...

## Slide 6: Requirements

## Slide 7: Specification
Line-in*
input()
Receiver
sample-in()
bit-out()
1
1
Transmitter
bit-in()
sample-out()
Line-out*
output()
1
1

## Slide 8: System architecture
Interrupt handlers for samples:
  input and output.
Transmitter.
Receiver.

## Slide 9: Transmitter
Waveform generation by table lookup.
  float sine_wave[N_SAMP] = { 0.0, 0.5, 0.866, 1, 0.866, 0.5, 0.0, -0.5, -0.866, -1.0, -0.866, -0.5, 0};
time

## Slide 10: Receiver
Filters (FIR for simplicity) use circular buffers to hold data.
Timer measures bit length.
State machine recognizes start bits, data bits.

## Slide 11: Hardware platform
CPU.
A/D converter.
D/A converter.
Timer.

## Slide 12: Component design and testing
Easy to test transmitter and receiver on host.
Transmitter can be verified with speaker outputs.
Receiver verification tasks:
  start bit recognition;
  data bit recognition.

## Slide 13: System integration and testing
Use loopback mode to test components against each other.
  Loopback in software or by connecting D/A and A/D converters.