## Slide 1: Program design and analysis
Digital still camera.

## Slide 2: Theory of operations
Taking a picture requires:
  Determining exposure and focus.
  Capturing the image.
  Developing the image.
  Compressing the image.
  Generating and storing an image file.
Luminance: brightness; chrominance: color.

## Slide 3: Bayer pattern

## Slide 4: Bayer pattern interpolation
Interpolate two missing color components for each pixel.
  Use values from neighbors.
R2.1 = (R1.0 + R1.1)/4
B2.1 = (B1.1 + B1.4)/2
G1.1 = (G1.1 + G2.1 + G2.2 + G1.4)/4

## Slide 5: Development algorithms
Color temperature correction: estimate color of light source and correct to normalize color values.
Sharpening algorithms reduce pixellation effects.

## Slide 6: Image compression
RAW images are uncompressed and usually uninterpolated.
  Formats are camera-dependent.
JPEG is lossy---relies on perceptual image coding.
  Eliminate or smooth some small features.

## Slide 7: JPEG compression process

## Slide 8: Color space conversion
Convert from RGB to luminance/chrominance form used in JPEG.
JFIF standard conversion matrix:

## Slide 9: Discrete cosine transform
Converts 8 x 8 block of pixel to spatial frequencies.
DCT computation is highly optimized, may be mapped onto accelerators or specialized instrutions.

## Slide 10: DCT quantization
DCT does not introduce loss.
  Quantizing the DCT matrix introduces loss.
Typical quantization matrix throws away high spatial frequencies:

## Slide 11: Generating the bit encoding
Zig-zag pattern reads coefficients from DC x,y spatial frequency to highest spatial frequency.
Increases opportunities for run-length encoding of 0s.

## Slide 12: File formats
TIFF generally used for uncompressed images.
EXIF adds information to image:
  Metadata (date, time, etc.).
  Thumbnail.
  JPEG data.
DCF specifies organization of directories, file names, etc.

## Slide 13: Camera platform architecture

## Slide 14: Picture taking process state diagram

## Slide 15: Picture taking process sequence diagram

## Slide 16: Picture viewing state diagram

## Slide 17: Camera class diagram

## Slide 18: Component design and testing
Image compression, file system, etc. may be obtained as intellectual property.
Multiple buffers in imaging pipeline can be used to help test the system.