## Slide 1: Processes and operating systems
Real-time operating systems.
Processes.
Scheduling policies:
  RMS;
  EDF.
Scheduling modeling assumptions.

## Slide 2: Operating systems
The operating system controls resources:
  who gets the CPU;
  when I/O takes place;
  how much memory is allocated.
The most important resource is the CPU itself.
  CPU access controlled by the scheduler.

## Slide 3: Process state
A process can be in one of three states:
  executing on the CPU;
  ready to run;
  waiting for data.
executing
ready
waiting
gets data
and CPU
needs
data
gets data
needs data
preempted
gets
CPU

## Slide 4: Operating system structure
OS needs to keep track of:
  process priorities;
  scheduling state;
  process activation record.
Processes may be created:
  statically before system starts;
  dynamically during execution.

## Slide 5: Embedded vs. general-purpose scheduling
Workstations try to avoid starving processes of CPU access.
  Fairness = access to CPU.
Embedded systems must meet deadlines.
  Low-priority processes may not run for a long time.

## Slide 6: Preemptive scheduling
Timer interrupt gives CPU to kernel.
  Time quantum is smallest increment of CPU scheduling time.
Kernel decides what task runs next.
Kernel performs context switch to new context.

## Slide 7: Context switching
Set of registers that define a process’s state is its context.
  Stored in a record.
Context switch moves the CPU from one process’s context to another.
Context switching code is usually assembly code.
  Restoring context is particularly tricky.

## Slide 8: freeRTOS.org context switch

## Slide 9: freeRTOS.org timer handler
void vPreemptiveTick( void )
{
/* Save the context of the current task. */
portSAVE_CONTEXT();
/* Increment the tick count - this may wake a task. */
vTaskIncrementTick();
/* Find the highest priority task that is ready to run. */
vTaskSwitchContext();
/* End the interrupt in the AIC. */
AT91C_BASE_AIC->AIC_EOICR = AT91C_BASE_PITC->PITC_PIVR;;
portRESTORE_CONTEXT();
}

## Slide 10: freeRTOS.org save context
push r0
in r0, __SREG__
cli
push r0
push r1
clr r1
push r2
; continue pushing all the registers
push r31
lds r26, pxCurrentTCB
lds r27, pxCurrentTCB + 1
in r0, __SP_L__
st x+, r0
in r0, __SP_H__
st x+, r0

## Slide 11: freeRTOS.org restore context
lds r26, pxCurrentTCB
lds r27, pxCurrentTCB + 1
ld r28, x+
out __SP_L__, r28
ld r29, x+
out __SP_H__, r29
pop r31
; pop the registers
pop r1
pop r0
out __SREG__, r0
pop r0

## Slide 12: Processes in UML
An active object has an independent thread of control.
Specified by an active class.

## Slide 13: Priority-driven scheduling
Each process has a priority.
CPU goes to highest-priority process that is ready.
Priorities determine scheduling policy:
  fixed priority;
  time-varying priorities.

## Slide 14: Priority-driven scheduling example
Rules:
  each process has a fixed priority (1 highest);
  highest-priority ready process gets CPU;
  process continues until done.
Processes
  P1: priority 1, execution time 10
  P2: priority 2, execution time 30
  P3: priority 3, execution time 20

## Slide 15: Priority-driven scheduling example
time
P2 ready t=0
P1 ready t=15
P3 ready t=18
0
30
10
20
60
40
50
P2
P2
P1
P3

## Slide 16: The scheduling problem
Can we meet all deadlines?
  Must be able to meet deadlines in all cases.
How much CPU horsepower do we need to meet our deadlines?

## Slide 17: Process initiation disciplines
Periodic process: executes on (almost) every period.
Aperiodic process: executes on demand.
Analyzing aperiodic process sets is harder---must consider worst-case combinations of process activations.

## Slide 18: Timing requirements on processes
Period: interval between process activations.
Initiation interval: reciprocal of period.
Initiation time: time at which process becomes ready.
Deadline: time at which process must finish.

## Slide 19: Timing violations
What happens if a process doesn’t finish by its deadline?
  Hard deadline: system fails if missed.
  Soft deadline: user may notice, but system doesn’t necessarily fail.

## Slide 20: Scheduling metrics
How do we evaluate a scheduling policy:
  Ability to satisfy all deadlines.
  CPU utilization---percentage of time devoted to useful work.
  Scheduling overhead---time required to make scheduling decision.

## Slide 21: Rate monotonic scheduling
RMS (Liu and Layland): widely-used, analyzable scheduling policy.
Analysis is known as Rate Monotonic Analysis (RMA).

## Slide 22: RMA model
All process run on single CPU.
Zero context switch time.
No data dependencies between processes.
Process execution time is constant.
Deadline is at end of period.
Highest-priority ready process runs.

## Slide 23: Process parameters
Ti is computation time of process i; ti is period of process i.
period ti
Pi
computation time Ti

## Slide 24: Rate-monotonic analysis
Response time: time required to finish process.
Critical instant: scheduling state that gives worst response time.
Critical instant occurs when all higher-priority processes are ready to execute.

## Slide 25: Critical instant
P4
P3
P2
P1
critical
instant
P1
P1
P1
P1
P2
P2
P3
interfering processes

## Slide 26: RMS priorities
Optimal (fixed) priority assignment:
  shortest-period process gets highest priority;
  priority inversely proportional to period;
  break ties arbitrarily.
No fixed-priority scheme does better.

## Slide 27: RMS optimality
Consider two processes with .
Case 1: If P1 (shorter period) has higher priority, then worst case is over P2’s period to execute P2 once and P1 as many times as required:
Case 2: If P2 (longer period) has higher priority, then worst case is to execute all of P2 and all of P1 in one of P1’s periods:
In some circumstances, second inequality cannot be satisfied but first can be.
In some circumstances, first inequality can be satisfied but second cannot be.
Therefore, it is always better to give the process with a shorter period the higher priority.
Use induction to generalize for processes.

## Slide 28: RMS example
time
0
5
10
P2 period
P1 period
P1
P2
P1
P1

## Slide 29: RMS CPU utilization
Utilization for n processes is
  S i Ti / ti
Given m tasks and ratio between any two periods less than 2:
As number of tasks approaches infinity, maximum utilization approaches 69%.

## Slide 30: RMS CPU utilization, cont’d.
RMS may not be able to use 100% of CPU, even with zero context switch overhead.
Must keep idle cycles available to handle worst-case scenario.
However, RMS guarantees all processes will always meet their deadlines.

## Slide 31: RMS implementation
Efficient implementation:
  scan processes;
  choose highest-priority active process.

## Slide 32: Earliest-deadline-first scheduling
EDF: dynamic priority scheduling scheme.
Process closest to its deadline has highest priority.
Requires recalculating processes at every timer interrupt.

## Slide 33: EDF analysis
EDF can use 100% of CPU.
But EDF may fail to miss a deadline.

## Slide 34: EDF implementation
On each timer interrupt:
  compute time to deadline;
  choose process closest to deadline.
Increasingly used in high-performance embedded systems to provide higher CPU utilization.
  Must verify that schedule is not overloaded.

## Slide 35: RMS vs. EDF
P1
P2
P3
RMS
EDF
0
6
12

## Slide 36: Fixing scheduling problems
What if your set of processes is unschedulable?
  Change deadlines in requirements.
  Reduce execution times of processes.
  Get a faster CPU.

## Slide 37: Race condition in shared memory
Problem when two CPUs try to write the same location:
  CPU 1 reads flag and sees 0.
  CPU 2 reads flag and sees 0.
  CPU 1 sets flag to one and writes location.
  CPU 2 sets flag to one and overwrites location.

## Slide 38: Atomic test-and-set
Problem can be solved with an atomic test-and-set:
  single bus operation reads memory location, tests it, writes it.
ARM test-and-set provided by SWP:
    ADR r0,SEMAPHORE
    LDR r1,#1
    GETFLAG SWP r1,r1,[r0]
    BNZ GETFLAG

## Slide 39: Semaphores
Semaphore: OS primitive for controlling access to critical regions.
Protocol:
  Get access to semaphore with P().
  Perform critical region operations.
  Release semaphore with V().

## Slide 40: Critical regions
Critical region: section of code that cannot be interrupted by another process.
Examples:
  writing shared memory;
  accessing I/O device.

## Slide 41: Priority inversion
Priority inversion: low-priority process keeps high-priority process from running.
Improper use of system resources can cause scheduling problems:
  Low-priority process grabs I/O device.
  High-priority device needs I/O device, but can’t get it until low-priority process is done.
Can cause deadlock.

## Slide 42: Solving priority inversion
Give priorities to system resources.
Have process inherit the priority of a resource that it requests.
  Low-priority process inherits priority of device if higher.

## Slide 43: Scheduling for low power
EDF with DVFS:
  First set the clock speed to meet the performance goal in the critical interval.
  Set clock speed for less-critical intervals in order of importance.
RMS with DVFS is NP-complete.
RMS/EDF with race-to-dark is currently handled with heuristics.

## Slide 44: Data dependencies
Data dependencies allow us to improve utilization.
  Restrict combination of processes that can run simultaneously.
P1 and P2 can’t run simultaneously.
P3 can preempt P1 or P2 but not both.
P1
P2
P3

## Slide 45: Context-switching time
Non-zero context switch time can push limits of a tight schedule.
Hard to calculate effects---depends on order of context switches.
In practice, OS context switch overhead is small (hundreds of clock cycles) relative to many common task periods (ms – ms).