## Slide 1: System design techniques
Design methodologies.
Requirements and specification.

## Slide 2: Design methodologies
Process for creating a system.
Many systems are complex:
  large specifications;
  multiple designers;
  interface to manufacturing.
Proper processes improve:
  quality;
  cost of design and manufacture.

## Slide 3: Product metrics
Time-to-market:
  beat competitors to market;
  meet marketing window (back-to-school).
Design cost.
Manufacturing cost.
Quality.

## Slide 4: Spacecraft design errors
Mars Climate Observer lost on Mars in September 1999.
Requirements problem:
  Requirements did not specify units.
  Lockheed Martin used English; JPL wanted metric.
Not caught by manual inspections.
New Horizons experienced 81-minute comm blackout while approaching Jupiter in 2015.
LightSail malfunctioned in orbit due to a file overflow bug.
  Bug occurred only after about 40 hours of operation, ground tests did not run long enough.

## Slide 5: Design flow
Design flow: sequence of steps in a design methodology.
May be partially or fully automated.
  Use tools to transform, verify design.
Design flow is one component of methodology. Methodology also includes management organization, etc.

## Slide 6: Waterfall model
Early model for software development:
requirements
architecture
coding
testing
maintenance

## Slide 7: Waterfall model steps
Requirements: determine basic characteristics.
Architecture: decompose into basic modules.
Coding: implement and integrate.
Testing: exercise and uncover bugs.
Maintenance: deploy, fix bugs, upgrade.

## Slide 8: Waterfall model critique
Only local feedback---may need iterations between coding and requirements, for example.
Doesn’t integrate top-down and bottom-up design.
Assumes hardware is given.

## Slide 9: Agile software design
Minimize time, cost of deployment.
  Reduced or eliminated requirements process.
  Reduced documentation.
  Simplified testing.
Often used in consumer-oriented software.
Does not provide documentation, testing required in many real-time embedded system applications.

## Slide 10: V model
product concept
manufacturing and operation
unit design
unit test
safety requirement verification
architecture
integration and system test
verification
Supports automotive safety methodologies.
Top-down design followed by bottom-up verification.

## Slide 11: Co-design methodology
Must architect hardware and software together:
  provide sufficient resources;
  avoid software bottlenecks.
Can build pieces somewhat independently, but integration is major step.
Also requires bottom-up feedback.

## Slide 12: Hierarchical design flow
Embedded systems must be designed across multiple levels of abstraction:
  system architecture;
  hardware and software systems;
  hardware and software components.
Often need design flows within design flows.

## Slide 13: Hierarchical HW/SW flow
spec
architecture
HW
SW
integrate
test
system
spec
HW architecture
detailed design
integration
test
hardware
spec
SW architecture
detailed design
integration
test
software

## Slide 14: Model-based design
Unified view of physical plant and embedded computing system (cyber plant).
Design created in domain-specific modeling language (DSML).
  Simulation.
  Design space exploration.
  Implementation synthesis.

## Slide 15: Requirements analysis
Requirements: a description of a desired system characteristic.
Specification: complete set of system requirements.
Requirements phase links customers with designers.

## Slide 16: Types of requirements
Functional: input/output relationships.
Non-functional:
  timing;
  power consumption;
  manufacturing cost;
  physical size;
  time-to-market;
  reliability.

## Slide 17: Eliciting requirements
Customer interviews.
Comparison with competitors.
Sales feedback.
Mock-ups, prototypes.
Next-bench syndrome (HP): design a product for someone like you.

## Slide 18: Use case
Defines example of user interaction with system.
Collection of use cases helps to define the system.

## Slide 19: CRC cards
Well-known method for analyzing a system and developing an architecture.
CRC:
  classes;
  responsibilities of each class;
  collaborators are other classes that work with a class.
Team-oriented methodology.

## Slide 20: CRC card format
Class name:
Superclasses:
Subclasses:
Responsibilities: Collaborators:
Class name:
Class’s function:
Attributes:
front
back

## Slide 21: CRC methodology
Develop an initial list of classes.
  Simple description is OK.
  Team members should discuss their choices.
Write initial responsibilities/collaborators.
  Helps to define the classes.
Create some usage scenarios.
  Major uses of system and classes.

## Slide 22: CRC methodology, cont’d.
Walk through scenarios.
  See what works and doesn’t work.
Refine the classes, responsibilities, and collaborators.
Add class relatoinships:
  superclass, subclass.

## Slide 23: CRC cards for elevator
Real-world classes:
  elevator car, passenger, floor control, car control, car sensor.
Architectural classes: car state, floor control reader, car control reader, car control sender, scheduler.

## Slide 24: Elevator responsibilities and collaborators

## Slide 25: Good specification
Correct.
Unambiguous.
Complete.
Verifiable: is each requirement satisfied in the final system?
Consistent: requirements do not contradict each other.

## Slide 26: Good specification, cont’d.
Modifiable: can update requirements easily.
Traceable:
  know why each requirement exists;
  go from source documents to requirement;
  go from requirement to implementation;
  back from implementation to requirement.

## Slide 27: Validating the specification
Validate spec to ensure correctness, completeness, consistency, etIc.
Specification bugs caught late in the design process are expensive to fix.
Validation techniques:
  Prototyping and user testing.
  Use cases.
  Formal methods.

## Slide 28: System modeling
Capture functional and non-functional properties:
  verify correctness of spec;
  compare spec to implementation.
Many specification styles:
  control-oriented vs. data-oriented;
  textual vs. graphical.
UML is one modeling/design language.

## Slide 29: Model-based design
Targets cyber-physical system = computing system + physical plant.
Methodology:
  Capture system in domain-specific modeling language (DSML).
  Validate using simulation, formal methods.
  Compile into implementation components:
    Software.
    Computing platform.
    Physical plant components.

## Slide 30: TCAS II specification
TCAS II: aircraft collision avoidance system.
Monitors aircraft and air traffic info.
Provides audio warnings and directives to avoid collisions.
Leveson et al used RMSL language to capture the TCAS specification.

## Slide 31: RMSL
State description:
Transition bus for transitions between many states:
state1
inputs
state description
outputs
a
b
c
d

## Slide 32: TCAS top-level description
CAS
power-off
power-on
Inputs:
TCAS-operational-status {operational,not-operational}
fully-operational
C
standby
own-aircraft
other-aircraft i:[1..30]
mode-s-ground-station i:[1..15]

## Slide 33: Own-Aircraft AND state
CAS
Inputs:
own-alt-radio: integer standby-discrete-input: {true,false}
own-alt-barometric:integer, etc.
Effective-SL
Alt-SL
Alt-layer
Climb-inibit
Descend-inibit
Increase-climb-inibit
Increase-Descend-inibit
Advisory-Status
...
...
...
...
...
...
...
1
2
7
...
1
2
7
Outputs:
sound-aural-alarm: {true,false} aural-alarm-inhibit: {true, false}
combined-control-out: enumerated, etc.

## Slide 34: SysML
Systems Modeling Language is based on UML.
Broad-spectrum systems engineering diagram.
Nine types of diagrams:
  Sequence (sd).
  State machine (stm).
  Package (pkg).
  Use case (uc).
  Block definition (bdd).
  Internal block (ibd).
  Activity (act).
  Requirement (req).
  Parametric (par).

## Slide 35: SysML use case diagram
drive car
perform maintenance
<<extend>>
cruise
warmup
<<extend>>
user
mechanic
uc ECUusecase [TopLevel]

## Slide 36: SysML block definition diagram
bdd ECU blocks
Sensors
Actuators
ControlLaw
<<system>> ECU

## Slide 37: SysML internal block diagram
ibd ECU block diagram
s: sensors
a: actuators
c: controlLaw

## Slide 38: SysML activity diagram
act ECU activity
start engine
warm-up
cruise
turn off
engine
engine
temp

## Slide 39: SysML requirement diagram
ECU functional
<<requirement>>
warm-up mode
ID = 1
provide warm-up
<<requirement>>
max RPM
ID = 2
maximum RPM 6000
+
+
req ECU requirements
ECU nonfunctional

## Slide 40: SysML parametric diagram
par ECU parameters
thr: throttle
fic: fuel injection control
f: inj
ni: integer
ni: integer
<<equal>>
<<equal>>

## Slide 41: MARTE
Targets model-based design of real-time embedded computing systems.
Non-Functional Properties Modeling (NFP) module captures non-functional properties.
Time Modeling (Time) model captures chronometric and sequential time characteristics.

## Slide 42: MARTE, cont’d.
High-Level Application Modeling (HLAM) profile describes quantitative and qualitative features.
Detailed Resource Modeling (DRM) profile provides for software, hardware resource modeling (SRM, HRM).
Generic Quantitative Analysis Modeling (GQAM) describes schedulability, performance analysis.
Performance Analysis Modeling (PAM) profile describes best-effort, soft real-time systems.

## Slide 43: Sequence diagram with MARTE timing constraint
sensors
control law
actuators
sd control cycle
{cpmin..cpmax}

## Slide 44: Object diagram with MARTE allocation annotations
ECU
control law
sensor values
actuator values
RTOS
<<sched resource>>
task
<<data resource>>
data
platform
<<compute resource>>
CPU
<<mem resource>>
mem
<<comm resource>>
bus
<<allocate>>
{kind=timeSched}
<<allocate>>
{kind=timeSched}
<<allocate>>
{kind=location}