## Slide 1: IoT systems
OSI model for networks.
Internet protocol.
IoT networking concepts.
Example networks:
  Classic Bluetooth, Bluetooth Low Energy.
  802.15.4 and Zigbee.
  Wi-Fi.

## Slide 2: Network abstractions
International Standards Organization (ISO) developed the Open Systems Interconnection (OSI) model to describe networks:
  7-layer model.
Provides a standard way to classify network components and operations.

## Slide 3: OSI model
physical
mechanical, electrical
data link
reliable data transport
network
end-to-end service
transport
connections
presentation
data format
session
application dialog control
application
end-use interface

## Slide 4: OSI layers
Physical: connectors, bit formats, etc.
Data link: error detection and control across a single link (single hop).
Network: end-to-end multi-hop data communication.
Transport: provides connections; may optimize network resources.
Session: services for end-user applications: data grouping, checkpointing, etc.
Presentation: data formats, transformation services.
Application: interface between network and end-user programs

## Slide 5: PHY and MAC
PHY = physical layer.
  Circuitry to transmit and receive bits.
MAC = media access control.
  Provides link-level services.

## Slide 6: Internet Protocol
Internet = network of networks.
  Transports data from one network to another.
The Internet uses Internet Protocol (IP).
  Isolated networks can also use IP.

## Slide 7
physical
data link
network
transport
presentation
session
application
Node A
physical
data link
network
physical
data link
network
transport
presentation
session
application
Node B
Router
Network links
Internet Protocol

## Slide 8
Data
Options and padding
Destination address
Source address
Time to live
Protocol
Header checksum
Identification
Flags
Fragment offset
Total length
Version
Header length
Service type
max 65,535 bytes

## Slide 9: IP routing
IP routing is best effort---no guarantees of packet delivery.
Build other services on top of IP:
  Use handshakes to verify delivery of packet.
  Network routers can enforce quality-of-service.

## Slide 10: Internet services
Domain name service (DNS):
  Map names onto IP addresses.
File transfer (FTP):
  Move files from machine to machine.
Terminal sessions:
  Telnet provides terminal-style access.
Web (HTTP):
  Built on top of FTP.
Email (SMTP):
  Built on top of FTP.

## Slide 11: Host-to-host service
Hides some details of IP:
  Break host communication into IP packets at source.
  Reassemble packets at destination.
  Use handshake to ensure packets arrive, retransmit if necessary.
Transmission Control Protocol (TCP):
  Connection-oriented service.
User Datagram Protocol (UDP):
  Datagram service.
  Datagram is modeled after telegram.

## Slide 12
Internet Protocol
Transmission Control Protocol
User Datagram Protocol
Simple Network Management Protocol
FTP
HTTP
SMTP

## Slide 13: IoT networking concepts
Edge device may not run IP protocol.
  IP connection may be provided by hub or gateway.
  Non-IP networks are known as edge networks.
Ad hoc network is self-organized---not set up by system administrator.
Ad hoc network services:
  Authentication of eligibility to join network.
  Authorization for access to given pieces of information on the network.
  Encryption and decryption.
Internet
gateway
device
device
device
message

## Slide 14: Network topologies
star
tree
mesh

## Slide 15: Routing
Routing discovery determines routes between source/destination pairs.
Routing is driven by routing tables at the nodes.
Routing table
Routing table
Routing table
Routing table
Routing table
Routing table
msg

## Slide 16: QoS
Many networks support synchronous and asynchronous communication.
  Asynchronous: data records, etc.
  Synchronous: voice, etc.
Quality-of-service (QoS): bandwidth and periodicity characteristics.
Admission control ensures that network can handle the QoS demands of a request.

## Slide 17: Synchronization and beacons
Many network operations require nodes to be synchronized.
Synchronization can be performed using beacon.
  Beacon transmission marks the beginning of a communications interval.
beacon
synchronous
asynchronous
…

## Slide 18: Communcations energy
Communications energy is a large part of node energy consumption.
Comm energy consumption depends on many factors and parameters.
  Generally evaluated for a set of use cases.
We can use power state machine to model communications energy cost.
sleep
idle
receive
transmit

## Slide 19: Communications power state machine example
sleep
1 mW
idle
50 mW
receive
25 mW
transmit
35 mW
step | state | time | energy
1 | sleep | 1 ms | 1 nJ
2 | idle | 10 ms | 0.5 nJ
3 | receive | 50 ms | 1.25 mJ
4 | transmit | 50 ms | 1.75 mJ
5 | receive | 50 ms | 1.25 mJ
6 | transmit | 50 ms | 1.75 mJ
 |  |  | total = 6 mJ

## Slide 20: Bluetooth
Introduced in 1999, originally for telephony applications.
Classic Bluetooth operates in instrumentation, scientific, and medical (ISM) band in the 2.4 GHz range.
Bluetooth networks organized as piconet.
  One master, several slaves.
  Slave can be active or parked.
  A device can be a slave on several networks simultaneously.

## Slide 21: Bluetooth stack
Transport protocol:
  Radio, baseband layer, link manager, logical link control and adaptation protocol (L2CAP).
Middleware:
  RFCOMM for serial port, service discovery protocol, Internet Protocol, IrDA, etc.
Applications.

## Slide 22: Bluetooth protocol
Every Bluetooth device has a 48-bit Bluetooth Device Address.
Every device has a Bluetooth clock.
Transmissions alternate between master and slave directions.
Two types of packets:
  Synchronous connection-oriented (SCO) packets for QoS-oriented traffic.
  Asynchronous connectionless (ACL) packets for non-QoS traffic.
  SCO traffic has higher priority than ACL packets.

## Slide 23: Bluetooth Low Energy
Designed for very low energy operation such as button-sized battery.
  Goal: minimize radio on-time.
Part of Bluetooth standard but deviates from Classic Bluetooth in several ways.
Advertising transmissions can be used to broadcast, discover devices, etc.
Connections can be established.
Attribute Protocol Layer allows devices to create application-specific protocols.
Generic Attribute Profile Layer (GATT) defines basic attributes for all BLUE devices.
Pairing devices uses a short-term key to send a long-term key.
  Bonding: storing long-term key in device database.
  Optional data encryption using AES.

## Slide 24
standby
initiating
advertising
connected
master
slave
scanning
active
passive

## Slide 25: 802.15.4 and ZigBee
802.15.4 defines MAC and PHY layers.
  Supports full-function and reduced-function devices.
  Either star or peer-to-peer topology.
  Communciation performed using frames.
  Optional superframe provides a beacon mechanism and QoS.
ZigBee is a set of application-oriented standards.
  NWK layer provides network services.
  APL layer provides application-level services.
  Supports many different topologies.

## Slide 26: Wi-Fi
Originally designed for portable and mobile applications.
  Has been adapted for lower-energy operation.
Supports ad hoc networking.
Network provides a set of services:
  Distribution of messages from one node to another.
  Integration delivers messages from another network.
  Association relates a station to an access point.