## Slide 1: Automotive and Aerospace Systems
Networked control.
Vehicular networks:
  CAN.
  TTP, FlexRay, etc.
Safety and security.

## Slide 2: Networked control
Computer networks that perform real-time control functions.
  Allows more computing power to be applied than is available from a single CPU.
  Allows processors to be physically near the devices they control.
Electronic control unit (ECU) is a digital unit in a car.
Line replaceable unit (LRU) is a module in an airplane avionics system.

## Slide 3: Vehicles as networks
1/3 of cost of car/airplane is electronics/avionics.
Modern cars may have 100+ processors and operate with 100 million lines of code.
Network applications:
  Vehicle control.
  Instrumentation.
  Communication.
  Passenger entertainment systems.

## Slide 4: Example automotive processors
Infineon XC2200 body control processor:
  16/32 bit processor.
  SRAM and EEPROM.
  Analog/digital converter.
  Pulse width modulator.
  Serial channels.
  Light drivers.
  Network connections.

## Slide 5: Freescale MPC5767R
Freescale MPC5767R for powertrain systems.
Dual-processor Power Architecture CPUs, including vector processors.
16K data and instruction caches.
Time processing unit used to generate and read waveforms.
CAN, Lin, FlexRay interfaces.

## Slide 6: Automobile network
Engine provides power to drive the wheels via the transmission.
Transmission adjusts gearing based on operating characteristics.
ABS controls brakes.

## Slide 7: Automotive network architectures
domain architecture
zone architecture

## Slide 8: Avionics
Avionics design must be certified.
Architectural evolution:
  Modular architecture has a separate LRU for each function (artificial horizon, engine control, etc.)
  Federated network has networks grouped by function (flight controls, navigation, etc.).
  Genesis Platform defines virtual avionics system that is mapped onto a physical network.

## Slide 9: CAN bus
First used in 1991.
Serial bus, 1 Mb/sec up to 40 m.
Synchronous bus.
Logic 0 dominates logic 1 on bus.
Arbitrated with CSMA/AMP:
  Arbitration on message priority.

## Slide 10: CAN data frame
11 bit destination address.
RTR bit determines read/write from/to destination.
Any node can detect bus error, interrupt packet for retransmission.

## Slide 11: CAN controller
Controller implements physical and data link layers.
No network layer needed---bus provides end-to-end connections.

## Slide 12: Other vehicle busses
Time-triggered architecture (TTA) assigns communications to time slots.
FlexRay is next generation:
  Time triggered protocol.
  10 Mb/s.
Local Interconnect Network (LIN) connects devices in a small area (e.g., door).
Passenger entertainment networks:
  Bluetooth.
  Media Oriented Systems Transport (MOST).

## Slide 13: Safety and security
Vehicles are safety-critical systems.
Threat models:
  Maintenance technicians may introduce problems either maliciously or accidentally.
  Component suppliers may supply components that don’t work with the system or include malware.
  Passengers may introduce malware either maliciously or accidentally.
  Passers-by may connect to vehicle wireless networks.

## Slide 14: Car hacking (1)
UCSD researchers demonstrated a variety of attacks that allowed them to gain complete control of a car.
Attack vectors:
  Infecting diagnostic computers used by mechanics.
  Using a specially-coded CD to load malware onto the CD player.
  Sending signals over the car’s telematics connection.

## Slide 15: Car hacking (2)
CMU researchers demonstrated a takeover of a Jeep Cherokee driven by a journalist.
Attack vector:
  Entered car through telematics systems.
  Entertainment system was then attacked and modified.
  Car components did not check the validity of software updates.
Entertainment system was used to send messages over CAN bus to kill engine, disable brakes.

## Slide 16: Car crashes
Oklahoma court ruled that Toyota was liable in a case of unintended acceleration.
  Electronic throttle control system source code contained 67 functinos with a cyclomatic complexity of over 50; throttle angle function had a cyclomatic complexity of 146.
  Car’s fail-safe capabilities were both inadequate and defective.

## Slide 17: Airplane hacking
A computer security researcher was arrested in 2015 on suspicion of having hacked into a Boeing 737 during a flight.
  Attack vector was through in-flight entertainment system.
  Allegedly modified code in the Thrust Management Computer.

## Slide 18: Software implicated in fatal airplane crash
Software bugs are suspected to have caused the crash of an Airbus A400M.
  Software in the ECUS are suspected to have caused three of four engines to shut down during flight.

## Slide 19: VW diesel defeat
VW admitted to installing a defeat of its own software on diesel cars.
  Defeat enabled strong emissions controls while car was being tested, disabled emissions controls during normal driving.