## Slide 1
Code and Instructions
http://www.marilynwolf.com
© 2025 Marilyn Wolf
Notes: This module describes the relationship between high-level langage code and instructions.

## Slide 2
Statement defines an action in a program.
Statements operate on variables.
Instructions are generated to implement statements.
Notes: Statement defines an action in a program.
Statements operate on variables.
Instructions are generated to implement statements.

## Slide 3
lw x28, 20(x2)
lw x29, 24(x2)
bge x28, x29, else1
addi x30, x28, 2
j done1
else1: addi x30, x29, 3
pc
Notes: Memory holds a sequence of instructions. The pc points to the currently executing instruction.

## Slide 4
Program counter (pc) points to current instruction.
A jump unconditionally changes pc.
A branch may change pc based on data or condition.
Notes: Program counter (pc) points to current instruction.
A jump unconditionally changes pc.
A branch may change pc based on data or condition.

## Slide 5
a = 1;
if (d > 5) {
b = 2;
} else {
b = 3;
}
w = a + b;
d = 3
d = 6
Notes: Different values of the variable d result in different execution paths through the program.

## Slide 6
blt x4, x5, lab2
lab1:
andi x4, x4, 7
lab2:
addi x3, x2, 5
aval:
.word 7
Notes: A label is a name for a location in an assembly language program.

## Slide 7
assembly
object
pass 1
pass 2
symbol table
Notes: Assembling a program into object code is a two-pass process. Pass 1 identifies the values assigned to labels and stores them in a symbol table. Pass 2 emits object code based on the symbol table.

## Slide 8
addi rd, rs, -15
lui rd, imm[31:12]
addi rd, rd, imm[11:0]
Notes: Some pseudoinstructions may be implemented in more than one instruction.

## Slide 9
object
binary
linker
object
object
object
symbol table
Notes: A linker combines several object modules into an executable binary. The symbol table may be included for debugging.

## Slide 10
a < b
b – a > 0
a – b < 0
Notes: Expressions may be rewritten to map directly into available instructions. For example, a < b can be written as either b – a > 0 or a – b < 0. The form most convenient for the instruction set can be chosen by the compiler.

## Slide 11
lw x29, 40(sp)
stack pointer
Notes: The stack pointer can be accessed with an offset, for example 40(sp).

## Slide 12
lw x28, a
lw x29, b
add x28, x28, x29
lw x27, c
mul x27, x27, x28
(a + b)*c
Notes: A single expression may result in several instructions to load variable values into registers and perform the required operations.

## Slide 13
lw x28, 44(sp)
lw x29, 48(sp)
add x3, x28, x29
sw x3, 52(sp)
a = b + c;
Notes: An assignment computes an expression on the right hand side of the assignment, then stores the value in the variable on the left hand side.

## Slide 14
bge x28, x29, else1
if1:
addi x30, x28, 0
j endif1
else1:
addi x30, x29, 0
endif1:
if (b < c) a = b; else a = c;
Notes: An if statement computes the test expression, then uses branches and jumps to execute the proper code based on the result.

## Slide 15
array1:
.word 0, 0, 0, 0
lw x30, 4(x10)
slli x31, x31, 2
add x30, x30, x31
lw x29, 0(x30)
Notes: To access an array, the index is first calculated. That index is then used as an offset from the base address of the array.

## Slide 16
whiletest:
bge x28, x27, whileexit
addi x28, x28, -1
j whiletest
whileexit:
while (i >= j) {
  i = i – 1;
}
Notes: A while statement computes the test function. The while loop body performs the required operations, then jumps back to the test.

## Slide 17
la x10, mystruct # starting address
lw x28, 0(x10) # index
lw x29, 4(x10) # value
struct record {
int index;
int value;
};
struct record mystruct;
Notes: Values in a struct can be accessed using constant offsets from a pointer.

## Slide 18
la x10, ptr
lw x29, 0(x10)
Notes: A pointer value can be loaded into a register, then the value is used to access the value being pointed to.

## Slide 19
forbody:
bge x28, x30, forexit
add x29, x29, x28
addi x28, x28, 1
j forbody
forexit:
for (i=0, sum = 0; i<N; i++)
sum = sum + i;
Notes: A for loop is similar to a while loop but with explicit loop initialization, tests, and update.

## Slide 20
<loop init>
while (<loop test>) {
< loop body>
<loop update>
}
for (<loop init>; <loop test>; <loop update>) {
<loop body>
}
Notes: The initialization code is executed before the loop proper is entered.

## Slide 21
return value
parameters
CPU status
local data
temporaries
Notes: A function activation record holds values used locally by the function: its return value, parameters, CPU status, local data, temporaries.

## Slide 22
initialize
load a[i], b[i]
d = d + a[i]*b[i]
update
i < n
result = d
T
F
Notes: A digital filter value is computed as a sum of a sequence of multiplied values. The operation can be implemented using a for loop.

## Slide 23
.data
# vector array declarations, declaration of size n, result
a: .word 1, 2, 3, 4
b: .word 3, 4, 2, 6
n: .word 4
result: .word 0
# initialize loop
la x24, a # current address in a
la x25, b # current address in b
li x26, 0 # temp
li x27, 0 # partial product
li x28, 0 # accumulation
li x29, 0 # loop counter
lw x30, n # vector size
Notes: The object code for the digital filter defines some storage for variables, then initializes the loop.

## Slide 24
.text
# loop
dotloop:
# access a[i]
lw x27, 0(x24)
# access b[i]
lw x26, 0(x25)
# multiply a[i] * b[i]
mul x27, x27, x26
# add to accumulated dot product
add x28, x28, x27
# update addresses in a, b
addi x24, x24, 4
addi x25, x25, 4
# update loop counter
addi x29, x29, 1
blt x29, x30, dotloop # done?
dotexit:
# store result
la x24, result
sw x28, 0(x24)
Notes: The loop body accesses a[i] and b[i], adds them into the running sum, and updates the array addresses and loop counter. It then tests the exit condition for the loop.

## Slide 25
Attack on program:
Inject malicious code as data.
Cause program to execute the malicious code.
Notes: Attack on program:
* Inject malicious code as data.
* Cause program to execute the malicious code.