## Slide 1
CPUs and Programming Models
http://www.marilynwolf.com
© 2025 Marilyn Wolf
Notes: This module explores the relationship between CPUs and the programming models they support.

## Slide 2
Programs store values in variables.
Computers store values in memory.
CPUs operate on data values in registers.
Notes: Programs store values in variables.
Computers store values in memory.
CPUs operate on data values in registers.

## Slide 3
Instruction set architecture:
Instructions format.
Instruction definition.
Data formats.
Notes: Instruction set architecture:
* Instructions format.
* Instruction definition.
* Data formats.

## Slide 4
von Neumann model:
Instructions and data in a unified memory.
CPU fetches and executes instructions.
Harvard model:
Separate instruction and data memories.
Notes: von Neumann model:
* Instructions and data in a unified memory.
* CPU fetches and executes instructions.
Harvard model:
* Separate instruction and data memories.

## Slide 5
memory
CPU
program counter
memory address
Notes: The CPU includes a program counter that defines the address of the currently executing instruction.
A memory address register holds the address of a location to be accessed.

## Slide 6
byte 0
byte 1
byte 2
byte 3
bit 0
byte 3
byte 2
byte 1
byte 0
bit 0
Notes: Endianness describes how bytes are ordered in a word.
A big-endian word puts bit 0 and byte 0 at the left-hand side of the word.
A little-endian word puts bit 0 and byte 0 at the right-hand side of the word.

## Slide 7
algebra | C language
 | a && b
 | a ¦¦ b
 | !a
 | a ^ b
algebra | C language
 | a && b
 | a ¦¦ b
 | !a
 | a ^ b
0 | 1
1 | 0
0 | 1
1 | 0
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: The C programming language provides several arithmetic and logical operators that correspond to traditional algebraic operators.
A truth table describes the output of a Boolean function for each combination of inputs. The tables describe not, AND, OR, XOR.

## Slide 8
association:
commutation:
distribution:
De Morgan:
double negation:
Notes: Several laws allow us to manipulate Boolean expressions: association, commutation, distribution, De Morgan, double negation.

## Slide 9
0 | 0 | 0
0 | 1 | 1
1 | - | 0
0 | 0 | 0
0 | 1 | 1
1 | - | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | X
input don’t care:
output don’t care:
Notes: An input don’t care is a shorthand for two input combinations that give the same output.
An output don’t care describes a partially-specified function whose output value is not defined for a certain input combination.

## Slide 10
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: A full adder performs two functions: sum and carry-out.
The sum is the exclusive or (XOR) of the three inputs ain, bin, cin.
The carry-out is true when at least two of the inputs are 1.

## Slide 11
Notes: We can write functions to chain several one-bit full adders into an n-bit full adder.

## Slide 12
Notes: Several functions are useful to describe arithmetic values:
Z is true if and only iff all of the input bits are 0.
A negative function is true if the most-significant bit of the word is 1.
A positive function is true if the word is not zero and not negative.
Two words can be compared bitwise with XOR functions to determine if they differ at any bit.

## Slide 13
 |  | (binary) | (binary) | 
Notes: An arithmetic overflow occurs when the top two carry out bits differ in value.

## Slide 14
Programming model:
All the bits that the programmer can see and manipulate.
CPU may use many registers that are not visible to the programmer.
Register varieties:
General-purpose registers.
Program counter.
Status register.
Special-purpose registers.
Notes: Programming model:
* All the bits that the programmer can see and manipulate.
* CPU may use many registers that are not visible to the programmer.
Register varieties:
* General-purpose registers.
* Program counter.
* Status register.
* Special-purpose registers.

## Slide 15
Register operand:
Value stored in a register.
Immediate operand:
Value in an instruction field.
Relative address:
Relative to an address in a register.
PC-relative address:
Relative to pc.
Effective address:
Final address after address calculation.
Absolute address:
An address in memory.
Notes: Register operand:
* Value stored in a register.
Immediate operand:
* Value in an instruction field.
Relative address:
Relative to an address in a register.
PC-relative address:
Relative to pc.
Effective address:
Final address after address calculation.
Absolute address:
An address in memory.

## Slide 16
x1 = 0xa04, imm = 4, PC = 0xc12, literal = 0xd34
Relative address for x1, imm: EA = 0xa04 + 4 = 0xa08
PC-relative address for PC, imm: EA = 0xc12 + 4 = 0xc16
Notes: Example: x1 = 0xa04, imm = 4, PC = 0xc12, literal = 0xd34
Relative address for x1, imm: EA = 0xa04 + 4 = 0xa08
PC-relative address for PC, imm: EA = 0xc12 + 4 = 0xc16

## Slide 17
byte 3
byte 2
byte 1
byte 0
byte 7
byte 6
byte 5
byte 4
byte 11
byte 10
byte 9
byte 8
Notes: In our example RISC-V machine, a word is four bites organized in little endian order.

## Slide 18
x1
x0: 0
x2
pc
x31
…
Notes: RISC-V includes 32 general purpose registers x0 through x31. The x0 register is a constant 0 whose value cannot be changed.
The program counter holds the location of an executing instruction.

## Slide 19
immediate
rs1
funct3
opcode
rd
R
immediate
rs1
funct3
opcode
rd
31
19
14
11
6
0
I
rs1
func3
opcode
immediate
immediate
rs2
S
imm[20]
imm[19:12]
opcode
rd
imm[10:1]
imm[11]
imm[12]
opcode
Imm[4:1], imm[11]
imm[10:5]
J
B
30
rs1
func3
rs2
20
Notes: An instruction format defines the meaning of bits in an instruction. Most CPUs have several different types of instructions, each with its own format.
We will look at five RISC-V instruction formats: R, I, S, J, B.

## Slide 20
1001
4
LW
6
LOAD
offset = 10012 = 910
rs1 = x4
rd = x6
14
x4: 27
x6: 14
mem[36]
lw
Notes: The lw instruction loads a word into a register. The address to load is given by adding an offset to the contents of a source register.

## Slide 21
4
SW
1001
STORE
offset = 10012 = 910
rs1 = x4
19
x4: 27
x6: 19
mem[36]
0
7
rs2 = x6
27 + 9 = 36
sw
Notes: A store word stores a word into memory from a register. The address to store is given by adding an offset to the contents of a source register.

## Slide 22
x5: 16
x7: 4
0000000
7
5
ADD
2
OP
x2: 20
rs2 = x7
rs1 = x5
rd = x2
x2 ¬ 16 + 4 = 20
add
Notes: An add instruction adds two values from registers and puts the result into a register.

## Slide 23
1001
5
ADDI
2
OP-IMM
imm = 10012 = 910
rs1 = x5
rd = x2
x5: 16
x2: 25
x2 ¬ 16 + 9 = 25
addi
Notes: An add immediate instruction adds a value from a register to an immediate value and puts the result in a register.

## Slide 24
x5: 7
x7: 5
0000000
7
5
XOR
2
OP
x2: 2
rs2 = x7
rs1 = x5
rd = x2
x2 ¬ 5 ^ 7 = 2
xor
Notes: An xor instruction performs the exclusive or of the values in two registers and stores the result in a register.

## Slide 25
x5: 4
x7: 2
0000000
7
5
SLL
2
OP
x2: 16
rs2 = 7
rs1 = x5
dest = x2
x2 ¬ 4 << 2 = 16
sll
Notes: A shift left logical performs a logical shift to the left on a value to a register. Zeros are filled in to the lower order bits. The result is stored in a register.

## Slide 26
1001
5
SLTI
2
OP-IMM
imm = 10012 = 910
rs1 = x5
rd = x2
x5: 16
x2: 0
x2 ¬ (16 < 9) == 0
slti
Notes: A set less than immediate compares a register value to an immediate. If the register value is smaller, it sets a value in a destination register.

## Slide 27
x3: 80
pc = 88
imm = 0 | 0 | 0 | 1102 | 0 = 11002
0
JAL
3
110
0
0
rd = 3
pc = 76 + 12 = 88
x3 = 76 + 4 = 80
jal
Notes: A jump and link instruction stores a return address known as a link, then changes the pc value to the jump location.

## Slide 28
x2: 12
0
BRANCH
0
imm = 1102
3
2
110
imm[11]
BEQ
x3: 12
pc = 76
pc = 64 + 12 = 76
rs1 = x2
rs2 = x3
beq
Notes: A branch if equal instruction compares two registers and changes the pc to a new value if the compared values are equal.

## Slide 29
Exception:
Unusual condition detected at run time.
Trap:
Action taken by CPU to respond to exception. Typically calls handler, may also halt.
Notes: Exception:
* Unusual condition detected at run time.
Trap:
* Action taken by CPU to respond to exception. Typically calls handler, may also halt.

## Slide 30
RISC-V execution modes:
User or application mode (U).
Supervisor mode (S).
Machine mode (M).
Notes: RISC-V execution modes:
* User or application mode (U).
* Supervisor mode (S).
* Machine mode (M).

## Slide 31
fetch
decode
execute
Notes: A simple model of instruction execution cycles through three stages: fetch the instruction, decode the instruction to determine its type and operands, execute the instruction.

## Slide 32
cpuword PC; /* program counter */
bit aluzero; /* set after arithmetic operation */
cpuword regfile[NREG]; /* register file */
cpuword IR; /* instruction register */
cpuword MA; /* memory address register */
cpuword MB; /* memory value register */
cpuword mem[MEMSIZE]; /* program memory */
Notes: We can create a C program to simulate the execution of instructions. CPU registers are represented by variables. Memory is represented as an array.

## Slide 33
void main() {
init_sim(); /* initialize the simulator internals */
init_prog_model(); /* initialize the programming model */
load(); /* load the image into the memory array */
do {
/* execute one instruction */
operate();
} while (!haltme());
}
Notes: The main program first reads the program to be simulated, then repeatedly performs an operation until a halt condition is encountered, either from an instruction or an external signal.

## Slide 34
void operate() { /* fetch, decode, execute current instruction */
/* fetch */
MA = PC;
MB = mem[MA];
IR = INSTR(mem[MA]);
/* decode and execute */
switch (OPCODE(IR)) {
case ADD_OPCODE:
execute_add(IR);
break;
/* other instruction cases */
}
}
Notes: The operate() function reads the current instruction from the memory array. A switch statement determines which opcode is to be executed. The cases of the switch specify how to execute each type of instruction.

## Slide 35
void execute_add(instr inst) {
/* extract the rs1, rs2, rdest values */
rdest = IR & (REGMASK << rd_offset);
rs1 = IR & (REGMASK << rs1_offset);
rs2 = IR & (REGMASK << rs2_offset);
regfile[rdest] = regfile[rs1] + regfile[rs2];
/* perform the add operation */
PC = ADRS(PC + 4); /* update PC */
}
Notes: As an example, execute_add() performs the operations on the registers as specified by the RISC-V instruction set.