## Slide 1
Hardware and Software
http://www.marilynwolf.com
© 2025 Marilyn Wolf
Notes: This module introduces basic concepts in computer engineering including both hardware and software.

## Slide 2
hub
data center
smartphone
cellular
Notes: Computers are everywhere: consumer devices like smartphones, home appliances, cars, personal computers, communication and networking systems, data centers.

## Slide 3
CPU
memory
I/O
bus
Notes: A computer system includes:
A central processing unit or CPU that executes instructions.
Memory to hold data and programs.
Input and output or I/O devices to interact with the outside world.
A bus or other interconnect to allow computer system components to interact with each other.

## Slide 4
Computers operate on data:
  Read data from memory or I/O device into the CPU.
  Operate on the value.
  Write result to memory or I/O device from the CPU.
Notes: Computers operate on data:
  Read data from memory or I/O device into the CPU.
  Operate on the value.
  Write result to memory or I/O device from the CPU.

## Slide 5
calculator application
user interface
math module
basic
business
scientific
abstraction
refinement
Notes: A computer application can be organized as a set of modules.
In this application, a calculator application consists of a math module and a user interface. The math module is in turn divided into basic, business, and scientific math modules.
Modules are refined from larger and more abstract to smaller and less abstract. In this case, calculator is refined into user interface and math modules.
The component modules and their relationships are organized in a hierarchy.
A module may be implemented in either software or hardware.

## Slide 6
Abstraction provides a simpler representation for a hardware or software object.
A hardware module is a collection of hardware components. A software module is a collection of software routines and data.
Hardware and software components can be organized as a hierarchy based on how they relate to each other.
A larger component or module can be decomposed into smaller units.
Abstraction and hierarchy help us practice divide-and-conquer.
Notes: Abstraction provides a simpler representation for a hardware or software object.
A hardware module is a collection of hardware components. A software module is a collection of software routines and data.
Hardware and software components can be organized as a hierarchy based on how they relate to each other.
A larger component or module can be decomposed into smaller units.
Abstraction and hierarchy help us practice divide-and-conquer.

## Slide 7
application
middleware
operating system
Notes: A layer diagram can be used to describe the organization of a computer system.
As an example, this computer system is organized into three layers:
The application layer is at the top.
A middleware layer in the middle provides services that can be used to build applications.
The operating system layer at the bottom manages computer system resources.
A layer may be implemented in hardware, software, or a combination.

## Slide 8
ctrl
p1
p2
om
Notes: A block diagram can be used to describe modules and their interconnections.
This example includes four modules: ctrl (short for control), p1, p2, om. Connections include:
Ctrl to p1.
Ctrl to p2.
Om to ctrl and p2.
Block diagrams are often used to describe hardware but may also be used to describe software.

## Slide 9
simple object diagram
a1: helper
h: config
c: controller
f: op_unit
diagram info
object: class
Notes: UML, the Unified Modeling Language, provides a number of diagram types to describe complex systems.
An object describes a module and the functions it provides.
A UML object diagram describes a set of objects and their interrelationships. An object includes name: class.
In this example, a: controller connects to a1: helper, h: config, and f:op_unit.
Two comments, diagram info and object: class, are include in boxes with folded corners.
A title for the diagram, simple object diagram, is included at the top-left corner of the box that includes the objects.
An object module is often used to describe software systems and may also be used to describe hardware.

## Slide 10
A
B
time
C
action1
response1
action2
response2
Notes: A UML sequence diagram describes the interaction of objects over time. Time is typically displayed vertically. A comment labels the vertical time direction.
The example includes three objects: A, B, C. Each object has a vertical timeline. A box on the timeline shows when the object is active. B first interacts with C: action1 from B to C, then response1 from C back to B. B and C then interact with A: action2 from B to A, then response 2 from A to C.

## Slide 11
read
operate
write
Notes: A UML state diagram shows the relationships between states of the system. A state is shows as a rounded box. Arrows show possible transitions from one state to another. A label may be provided to show the condition under which a transition occurs. A label may also show the output generated at a transition.
This example includes three states: read, operate, write. Transitions go from read to operate, operate to write, and write back to read.

## Slide 12
setup
operate
x > 3
[ true ]
[ false ]
start
end
x
Notes: This example shows a more complex UML state diagram.
The start is shown as a circle, the end is shown as two concentric circles. Comments describe the start and end nodes.
The start transitions to the setup state, which then transitions to operate.
When a value x is received, operate transitions to a conditional that tests whether x > 3. If not, a transition is taken to the end. If true, a transition is taken back to the operate state.

## Slide 13
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
0/1
…
7
6
5
4
n-1
0
3
2
1
0
bit
byte
n-bit word
Notes: A bit is a basic unit of information in a computer. A bit is a binary value whose state can be represented by 0 (false) or 1 (true).
A byte is a sequence of eight bits.
A word is a sequence of bits. Different computer systems use different word lengths.

## Slide 14
7
14
3
999
…
location 0
location 1
location 2
address
location 2b-1
Notes: Computer memory is organized as an array of words. Each location is specified by an address. The word at a given address has a value.

## Slide 15
Bits/bytes/words can represent:
  A logical value or vector of logical values.
  A number.
  A character.
  An instruction.
  An address in memory.
Notes: Bits/bytes/words can represent:
  A logical value or vector of logical values.
  A number.
  A character.
  An instruction.
  An address in memory.

## Slide 16
Instruction set architecture:
Describes the operations provided by the computer.
Microarchitecture:
A structure that executes instructions.
Synchronous logic is governed by a clock signal.
Notes: Instruction set architecture:
Describes the operations provided by the computer.
Microarchitecture:
A structure that executes instructions.
Synchronous logic is governed by a clock signal.

## Slide 17
Algorithm:
A sequence of abstract operations designed to perform a desired function.
Instruction:
An operation on a computer.
Program:
A set of instructions and data that perform an algorithm on a computer.
Notes: Algorithm:
A sequence of abstract operations designed to perform a desired function.
Instruction:
An operation on a computer.
Program:
A set of instructions and data that perform an algorithm on a computer.

## Slide 18
lw x28, 44(sp)
lw x29, 48(sp)
bge x28, x29, else1
if1:
addi x30, x28, 0
j endif1
else1:
addi x30, x29, 0
endif1:
if (b < c)
a = b;
else
a = c;
C program
instructions
Notes: C is a widely-used programming language known as a high-level language. Many other high-level programming languages are also in widespread use.
A CPU does not directly execute a high-level language program. The program must be translated into instructions and data for execution by the CPU. Compilers are applications that translate programs into executable form.

## Slide 19
program
input device
output
input
output device
output
input
Notes: This sequence diagram illustrates input and output operations.
Three objects in this diagram include a program, an output device, and an input device. The program sends data to the output device to trigger output actions. The program receives data from the input device.

## Slide 20
Notes: Digital logic is used to operate on bit values.
A NAND gate performs a not(AND) operation. A NOR gate performs a not(OR) operation.
The upper NAND gate is connected to primary inputs i1, i2. The lower gate is connected to primary inputs i2, i3. The NOR gate is connected to the two outputs fo the NAND gates. The outputs of the upper NAND gate and the NOR gate are provided as primary outputs.

## Slide 21
CPU
memory
keyboard
storage
display
webcam
mouse
Notes: A more complete view of a personal computer system includes:
A CPU.
Memory for instructions and data.
Storage for programs and other information.
A keyboard, mouse, and webcam as input devices.
A display as an output device.

## Slide 22
Notes: This photograph shows two small embedded computers: a Raspberry Pi and an Arduino.

## Slide 23
kernel
user interface
file system
networking
Notes: This layer diagram describes the basic software organization of a computer operating system:
The kernel at the bottom layer provides core functions for scheduling programs and input/output operations.
Three layers build on the kernel:
  User interface provides convenient input and output for a user.
  A file system stores data.
  Networking communicates with other computers.

## Slide 24
Characteristics of computer systems:
Power and energy consumption.
Reliability and mean time between failures (MTBF).
Programmability.
Manufacturing costs.
Characteristics can be traded-off during design, sacrificing one characteristic to improve another.
Notes: Characteristics of computer systems:
Power and energy consumption.
Reliability and mean time between failures (MTBF).
Programmability.
Manufacturing costs.
Characteristics can be traded-off during design, sacrificing one characteristic to improve another.

## Slide 25
sketch
LED
dot
dash
Notes: This sequence diagram shows the operation of a simple Ardunio program. The program flashes a Morse code character on the board LED: first a short flash known as a dot, then a longer flash known as a dash. This dot-dash represents the character A in Morse code.
The sketch turns the LED on and off to show the dot followed by the dash. It repeatedly flashes the dot-dash sequence.

## Slide 26
host
target
Notes: Because the Arduino is a simple computer, we develop programs for it using a larger host computer.
The figure shows a host computer connected to a target Arduino connected by a cable.

## Slide 27
Notes: This figure shows an Arduino window on the host that displays the program blink_morse.ino.

## Slide 28
if (a < b) {
maxval = b;
} else {
maxval = a;
}
int max(int a, int b) {
if (a > b) return a;
else return b;
}
Notes: The left-hand C code performs two different operations based on the result of testing a < b: the variable maxval is set to b if the test is true, maxval is set to a if the test is false.
The right-hand C code shows the code as a function max() that takes two inputs a, b and returns a or b, depending on the outcome of the a > b test.

## Slide 29
void setup() {
// initialize LED as output
pinMode(LED_BUILTIN, OUTPUT);
}
Notes: A setup function initializes the Arduino board’s LED function using pinMode().

## Slide 30
sketch
LED
timer
dot
short
dash
long
dash
dot
short
long
space
space
space
delay(delaycount); // delay for delaycount ticks
Notes: A timer on the Arduino is used to measure the length of a dot or dash, the time between dots/dashes, and the time between characters.
This sequence diagram shows the interaction between the sketch, the Arduino timer, and the LED. The timer is used to emit a dot using a short time, then a dash using a long time. The dot/dash sequence is repeated.

## Slide 31
void loop() {
// this function runs repeatedly
// blink dit space dah space
// dit
digitalWrite(LED_BUILTIN, HIGH); // turn on LED
delay(500); // leave LED on 500 ticks
digitalWrite(LED_BUILTIN, LOW); // turn off LED
// space
delay(500); // wait 500 ticks
// dah
digitalWrite(LED_BUILTIN, HIGH); // turn on LED
delay(1000); // leave LED on 1000 ticks
digitalWrite(LED_BUILTIN, LOW); // turn off LED
// space
delay(500); // wait 500 ticks
/// and repeat...
delay(500); // wait
}
Notes: The Arduino loop function is called repeatedly to perform the basic operations of the application.
The dot/dash are emitted repeatedly by the loop() function.

## Slide 32: Digital abstraction
in
out
in
out
time
1
0
1
1
0
0
Notes: Digital circuits operate on continuous values. We abstract those continues values to discrete digital values.
The inverter on the left has one input and one output. The output is the logical complement of the input.
The continuous input and output signals are shows as a function of time on the right. We can assign digital values to regions of the signals.

## Slide 33: Sequential logic
D
Q
clock
in
Notes: We use registers to hold values so that we can operate on them later.
The figure shows a register with a D data input and Q data output. A clock input controls when it reads the D input and saves its valuie. The Q output is connected to one input of a NAND gate whose other input comes from elsewhere. The NAND gate’s output is connected to the register’s D input.

## Slide 34: Hierarchical design
datapath
controller
register file
Notes: Hierarchical design allows us to break a complex system into pieces.
This example consists of two modules: datapath and controller. The datapath is further shows as decomposed into several smaller components.

## Slide 35: Memory and storage
Memory stores data and instructions for execution on the CPU. Storage holds data, programs, and operational information.
Memory requires power to retain values. Storage retains values even when power is not applied.
Modern memory and storage components provide huge capacity with high reliability.
Notes: Memory stores data and instructions for execution on the CPU. Storage holds data, programs, and operational information.
Memory requires power to retain values. Storage retains values even when power is not applied.
Modern memory and storage components provide huge capacity with high reliability.

## Slide 36: Programming languages
CPUs execute instructions. Directly implementing an application using instructions requires time and effort.
Programming languages provide abstract models for programs. Compilers and interpreters translate a program into executable code and data.
Notes: CPUs execute instructions. Directly implementing an application using instructions requires time and effort.
Programming languages provide abstract models for programs. Compilers and interpreters translate a program into executable code and data.

## Slide 37: Operating systems
The operating system manages computer system resources:
Program execution.
Data storage.
Networking.
User interface.
Notes: The operating system manages computer system resources:
* Program execution.
* Data storage.
* Networking.
User interface.

## Slide 38: Networks
Computer networks allow computers to communicate with each other.
Software abstractions allow different types of comptuers and networks to interoperate.
Notes: Computer networks allow computers to communicate with each other.
Software abstractions allow different types of comptuers and networks to interoperate.