## Slide 1
Input and Output
http://www.marilynwolf.com
© 2025 Marilyn Wolf
Notes: This module introduces basic concepts in input and output.

## Slide 2
Read data from input device.
Operate on data using CPU.
Write data to output device.
Notes: Read data from input device.
Operate on data using CPU.
Write data to output device.

## Slide 3
status
data
device handler
CPU
device
Notes: A typical I/O device includes two types of registers: status and data. The status register is used to control the device. The data register holds data for input or output.

## Slide 4
device 0
device 1
main program
Notes: Memory-mapped I/O assigns memory addresses to the registers of a device. Each device has its own set of locations assigned in memory.

## Slide 5
while (!status) ; /* do nothing */
mydata = device_data;
Notes: A simple read loop tests the status of an input device. When status is 1, the device data is assigned to a variable.

## Slide 6
a = 1;
if (d > 5) {
b = 2;
} else {
b = 3;
}
w = a + b;
void handler() {
mydata = device[0];
device[1] = 0;
}
Notes: An interrupt mechanism allows the CPU to respond to a device request. A device handler can execute to operate on a device, then return to the program.

## Slide 7
fetch
decode
execute
push pc
pc = vector
interrupt?
Notes: At the start of the execution of an instruction, the CPU first checks whether an interrupt is pending. If so, the current pc is stored onto a stack and the pc is assigned a vector corresponding to the handler for the device. The fetch/decode/execution sequence then continues.
When the handler is finished, it executes instructions to restore the interrupted pc value from the stack.

## Slide 8
Interrupt priority determines which interrupt is handled first.
Interrupt vector determines what driver/handler is used to service the interrupt.

## Slide 9
if (switch1) led1 = 1;
else led1 = 0;

## Slide 10
stop bit
UART
physical I/O
device
serial link
time
bit 0
bit n-1
…
start bit
computer
sync 1
sync 2
command
mode
transmitter buffer
status
receiver buffer

## Slide 11
computer
UART
serial line
transmit
receive
mode
character
status
character