## Slide 1
Register-Transfer and Finite-State Machines
http://www.marilynwolf.com
© 2025 Marilyn Wolf

## Slide 2
Register stores a value.
Register writing is controlled by a clock.
Register value is stable except for a small window.

## Slide 8
time
T

## Slide 9
D
Q
clock
D
Q
D
Q
t1
t2
t3

## Slide 10
time

## Slide 22
always @(posedge clk)
begin
Q <= D;
end;

## Slide 23
module simple_register(
input clk,
input D,
output reg Q
);
always @(posedge clk)
begin
Q <= D;
end
endmodule

## Slide 24
D
Q
D
Q
D
Q
D
Q
D
Q
combinational logic

## Slide 25
regb
D
Q
rega
D
Q
regc
D
Q
regy
D
Q
regz
D
Q
combinational logic
tay
taz
tby
tbz
tcy
tcz

## Slide 26
module shift_register(
input clk,
input reset,
input shiftin,
output reg shiftout
);
reg [1:0] bits;
always @(posedge clk or posedge reset)
begin
if (reset)
begin
bits = 2'b00;
end
else begin
shiftout <= bits[1];
bits[1] <= bits[0];
bits[0] <= shiftin;
end
end
endmodule

## Slide 27
module two_bit_rt(
input clk,
input reset,
input incr,
output reg done
);
reg [1:0] state;
always @(posedge clk or posedge reset)
begin
if (reset)
begin
state <= 2'b00;
done <= 1'b0;
end
else begin
state <= state;
done <= 1'b0;
if (incr)
begin
state <= state + 1'b1;
done <= (state == 2'b11);
end
end
end
endmodule

## Slide 28
0
1
2
3
0 / 0
0 / 0
0 / 0
0 / 0
1 / 1
1 / 0
1 / 0
1 / 0
incr / done

## Slide 29
module two_bit_counter(
input clk,
input reset,
input incr,
output reg done
);
reg [1:0] state;
always @(posedge clk or posedge reset)
begin
if (reset)
begin
state <= 2'b00;
done <= 1'b0;
end
else begin
done <= 1’b0;
end
end
endmodule
case (state)
2'b00:
if (incr)
state <= 2'b01;
else
state <= 2'b00;
2'b01:
if (incr)
state <= 2'b10;
else
state <= 2'b01;
2'b10:
if (incr)
state <= 2'b11;
else
state <= 2'b10;
2'b11:
if (incr)
begin
state <= 2'b00;
done <= 1'b1;
end
else
state <= 2'b11;
endcase

## Slide 30
D
Q
D
Q
+
done
incr
0
1
clock
clock

## Slide 31
coin
vend 1
vend 2
vending machine
FSM
product 2
product 1

## Slide 34
input (coin, product 1, product 2) | state | next | output (vend 1, vend 2)
1-- | none | one | 00
10 - | one | two | 00
0-- | none | none | 00
0-- | one | one | 00
0-- | two | two | 00
01- | one | none | 10
001 | two | none | 01
010 | two | one | 10

## Slide 35
input (coin, product 1, product 2) | state | next | output (vend 1, vend 2)
1-- | 00 | 10 | 00
10 - | 01 | 10 | 00
0-- | 00 | 00 | 00
0-- | 01 | 01 | 00
0-- | 10 | 10 | 00
01- | 01 | 00 | 10
001 | 10 | 00 | 01
010 | 10 | 01 | 10

## Slide 36
module vending_encoded(
input clk,
input reset,
input coin, product1, product2,
output reg vend1, vend2
);
reg [1:0] state;
parameter none = 2'b00,
one = 2'b01,
two = 2'b10;
always @(posedge clk or posedge reset)
begin
if (reset)
begin
state <= none;
vend1 <= 1'b0;
vend2 <= 1'b0;
end
else begin
case (state)
none:
begin
vend1 <= 1'b0;
vend2 <= 1'b0;
if (coin)
begin
state <= one;
end
end
one:
begin
vend1 <= 1'b0;
vend2 <= 1'b0;
if (coin)
begin
vend1 <= 1'b0;
vend2 <= 1'b0;
state <= two;
end
else if (!coin && product1)
begin
vend1 <= 1'b1;
vend2 <= 1'b0;
state <= none;
end
end
two:
begin
vend1 <= 1'b0;
vend2 <= 1'b0;
if (product2)
begin
vend1 <= 1'b0;
vend2 <= 1'b1;
state <= none;
end
else if (product1)
begin
vend1 <= 1'b1;
vend2 <= 1'b0;
state <= one;
end
end
endcase
end
end
endmodule